## Slide 1
SideWork D2: Converting Linear to Rotational Motion
It is common to convert linear motion of a piston to rotational motion of a shaft by the use of a connecting rod. In the schematic shown, a piston rides in a frictionless cylinder. One side of the piston is exposed to a load P. A connecting rod (BC) of length L connects the other end of the piston to a crank arm of length r.
A counter-clockwise restraining moment or torque (M) is applied to the crank arm of length r, which has a crank angle q with respect to the vertical angle at the instant shown. The crank rotates with a constant angular speed (w = dq/dt) clockwise. Treating all components as massless, analyze and determine as a function of time:
All reaction forces (at piston and A)
The applied torque (M)
EXTRA CREDIT:
Determine the speed and acceleration of the piston
WRITE A MATLAB SCRIPT THAT PRODUCES WELL-FORMATTED PLOTS. USE DEFAULT PARAMETER VALUES P = 1kN, L = 0.15m, r = 0.07m, w = (2000rev/min)*2p
SUMBIT FILE TO TEAMS. Use the filename “NAME_SideWork_D2”
Notes: <number>